## Slide 1: Domain 4 Communication and Network Security Wireless security Lunch & Learn ISC2 Chapter – US military Wiesbaden Ingo Rosenbaum

## Slide 2: Agenda:
Wi-Fi Basics – Physical and Network
Wi-Fi History
Wi-Fi Components and Topology
Wireless Security Issues
Attack Vectors, Threats and Vulnerabilities
Protection and Hardening
Outlook
FAQs

## Slide 3: Wi-Fi Basics – Physical and Network
Wireless LAN is a radio transmitting and receiving technology.
It is based on the Theory of electromagnetic fields (Hertz, Maxwell et.al) which describes the effect of alternating current flows through a wire, a magnetic field is generated around that wire.
Basics:
Wavelength (m): Lambda λ
Lightspeed c=299.792.458 m/s
Frequency (Hz) f
Energy E
Plancks natural constant h=6,626 x 10-6 Js or 6,582 x 10-16 eV
Wavelength λ is indirect proportional to the frequency f
Wavelength: λ =
Energy: E = h*f
The Electromagnetic Spectrum refers to the full range of all possible Electromagnetic Field energy frequencies. This energy traveling through space is called radiation.

## Slide 5: WLAN – RF Modulation and Bandwith
WI-FI is operating in the ISM Band (Industrial, Scientific, Medical)
Ranges from 2.4 GHz up to 5.8 GHz
Fundamentals: Amplitude-/Frequency-/Phase-Shift- Keying
Frequency Hoppying Spread Spectrum FHSS
Direct Sequence Spread Spectrum DSSS
Orthogonal Frequency-Division Multiplexing OFDM
Notes: FCC – US opened 2.4 – 5.8 GHz in the US
5.2 GHz opened by ETSI for HyperLan in Europe
Digital by nature does not need a carrier wave – for inteference, noise reduction, very low/limited bandwith capacity
OFDM uses binarey phase shift keying BPSK and quadrature phase shift keyeing QPSK phase modulateion for the lower OFDM data rates
The higher OFDM data rates use 16-QAM and 64 QAM modulation
Quadrature Amplitude Modulation – QAM – is a phbrid of phase and amplitude modulation

## Slide 6: OFDM – Current standard
OFDM is NOT a spread spectrum technology
Multicarrier Frequency Domain Multiplexing Modulation Technology
Orthogonal… what the heck does this mean?
  In Mathematics it has got multiple meanings:
    Two segments are „orthogonal“ to each other if they form a right angle
    By extension, orthogonality is used to refer to the seperation of specific features of a system
      Euclidean vector spaces
      Orthogonal integral functions etc.
In communications, multiple-access schemes are orthogonal when an ideal receiver can completely reject arbitrarily strong unwanted signals from the desired signal using different basis functions.

## Slide 7: OFDM
Notes: Time and Frequency are orthogonal…. At one time a QAM Symbol carries over different frequency-Sub carrieres …
Robust performance agains narrow-band interference
Long symbol duration

## Slide 8: WI-FI History 1/3
IEEE 802.11 – September 1997
  Specs for PHY and MAC Layer (ISO-OSI)
IEEE 802.11a – September 1999
  5GHz, 54MBit/s – OFDM => Regul. Restriction in some Countries
IEEE 802.11b – December 1999
  2,4GHz, 11MBit/s – DSSS => Widely adopted e.g. Apple iBook plus AirPort Support
IEEE 802.11g – June 2003
  2,4GHz, 54MBit/s – OFDM ->
  Transmit Power Control TPC
  Dynamic Frequence Selection DFS
Notes: TPC (Transmit Power Control) reduziert ähnlich wie bei Mobiltelefonen die Sendeleistung abhängig von der Notwendigkeit (guter Kontakt zwischen den Geräten = geringere Sendeleistung).
DFS (Dynamic Frequency Selection): Es wird selbstständig eine freie Frequenz gewählt, z. B. um das Stören von Radaranlagen zu vermeiden.

## Slide 9: WI-FI History 2/3
IEEE 802.11n – September 2009
  Dual Band (2,4 and 5GHz), 600MBit/s MIMO-OFDM, Transmitting of different Signals at the same time ->Spatial Streams 4x4:4 -> 1st number: max number of Transmitting Antennas
  2nd number: max. number of Receiving Antennas
  3rd number: max.number of Spatial Streams
IEEE 802.11ad – December 2012
  Wireless Gigabit (WiGig), Operation Range 57-66GHz
  Transition between WLAN-WPN -> short distance but High Throughput (4K-HDR with 60fps)

## Slide 10: WI-FI History 3/3
IEEE 802.11ac – December 2013
  5GHz only, New Concept of „WAVE“ means new standards and Technology implementation -> Bandwith up to 3,4GBit/s
  WAVE 2 –Multi-User MIMO – MU-MIMO
  Beamforming
IEEE 802.11ax– January 2020
  Wi-Fi 6 – 5GHz, up to 4,8Gbit/s 8x8 OFDMA
  Backwardcompatible to older standards a,b,g,n,ac
  IoT applications
Notes: Orthogonal frequency-division multiple access

## Slide 11: Additional Standards
IEEE 802.15 – Bluetooth WPAN 2,4GHz, max. 100mW -> 5-20m Range
IEEE 802.15.4 – ZigBee Smart Home
IEEE 802.16 – WiMax – WAN–Wi-Fi
  Frequency Range: 2-66 GHz up to 1GBit/s
  Max. Transmitpower: 30W
  Operational Range: up to 50km

## Slide 12: IEEE 802.11w
IEEE 802.11w -> Protected Management Frame (2009)
Concept for encrypted and cleartext management exchange frames between STA and AP
Encrypted PMF:
  Disassociation
  Deauthentication
    Both execute the termination of a connection:
  Action-Frames (e.g. Channel Switch Announcement)
  802.11k-Frames ( Radio Measurement Action for Infrastructure BSS)
Notes: https://en.wikipedia.org/wiki/IEEE_802.11w-2009

## Slide 13: IEEE 802.11w
Non-Encrypted PMF:
  Beacon: permanent sending SSIDs and status frames
  Probe Request and Response: Active probing frames sending from STA to AP
  Association Request and Response: Information exchange about synchronization and datarate
  Re-association Request and Response: Information exchange about better AP range ->Roaming
  Announcement Traffic Indication Message
  Authentication -> usually first request open, due to Challenge-Response „go-for“ encryption

## Slide 14: IEEE 802.11w
Broadcast Frames are non-encrypted
802.11w gets rid of „Spoofed Disconnect“ DoS attacks resulting from spoofing of
  Deauth / Disassoc / Assoc Request or
  Auth Request in existing connection
Certain „Action Managment Frames“ are also made anti-spoofing
  Spectrum Management, QoS, BlockAck, Radio Measurement, Fast BBS Transition
ATTENTION: In many clients PMF is deactivated or not supported
Notes: Where does the shared secret key come from
It is derived using EAPOL 4-way handshake between AP and Client
This also means that 802.11w can only be used if you are using WPA or WPA2
Broadcast/multicast management frames are protected using a key called Integrity Group Temporal Key (IGTK)
Unicast management frames are protected using WPA/WPA2 pair-wise encryption key (PTK)

## Slide 15: Wi-Fi Components and Topology
WNIC: Wireless Network Interface Card
  Mostly inbuild in STA, older implemetation are based on PCMCIA, SmartCards Modules or USB Dongle
STA:
  Stations (Computer, Laptops, Smartphones, Tablets, IoT-Devices, etc.)
Access Points:
  Networking hardware device allowing WI-FI Stations/Devices to connect to a wired network
WLAN/Wi-Fi Controller:
  Management and Configuration of Enterprise Wi-Fi Networks
Notes: RADIUS is an AAA protocol that manages network access. AAA stands for authentication, authorization and accounting. RADIUS uses two packet types to manage the full AAA process; Access-Request, which manages authentication and authorization; and Accounting-Request, which manages accounting. Authentication and authorization are defined in RFC 2865 while accounting is described by RFC 2866.
WLAn Controller – Managemetn and Configuration
Interference Mitigation:
Load Balancing
Radio Balancing
Fail over:
RF Visualization
Mesh Connectivity

## Slide 16: Wi-Fi Topology
IBSS: Independet Basic Service Set
  Ad-hoc Network, 2 or more STA connects directly without AP
BBS: Basic Service Set
  Stations connect to an Access Point. Max. 100 Clients per AP, AP is connected via Ethernet to Network
ESS: Extended Service Set
  More than one AP is connected to the Ethernet. Roaming available – Site-Survey essential
WDS: Wireless Distribution Service
  Repeater – receive weak signal, amplify and resend
Notes: RADIUS is an AAA protocol that manages network access. AAA stands for authentication, authorization and accounting. RADIUS uses two packet types to manage the full AAA process; Access-Request, which manages authentication and authorization; and Accounting-Request, which manages accounting. Authentication and authorization are defined in RFC 2865 while accounting is described by RFC 2866.
WLAn Controller – Managemetn and Configuration
Interference Mitigation:
Load Balancing
Radio Balancing
Fail over:
RF Visualization
Mesh Connectivity

## Slide 17
WI-FI Security

## Slide 18: Wireless Security Issues
No Cable .. Direct and open access to radio signal
=> Easy Sniffing, only weak signal or radio transmitting protection/shielding mechanism can work
First Implementation of Wi-Fi -> very weak security (WEP)
No or very weak authentication – SSID as a name for a Wi-Fi network is easy to detect and often in cleartext

## Slide 19: WEP Security Issues
Wired Equivalent Protection WEP – Intro in 1997 and ratified as a Wi-Fi security standard in 1999
Intended confidentiality comparable to Wired Network
Uses stream cipher RC4 for confidentiality and CRC-32 checksum for integrity
64-bit, 128-bit, 152-bit and 256-bit Key implementations are available
Very simple encryption scheme – RC4 Keystream XORed with Plaintext

## Slide 20: WEP Security Issues
2 Authentication Methods available:
  Opens System Auth No authentication occurs as STA does not provide credentials to AP
  Shared Key Auth – WEP key is used – 4-step challenge response handshake:
    1. The client sends an authentication request to the Access Point.
    2. The Access Point replies with a clear-text challenge.
    3. The client encrypts the challenge-text using the configured WEP key and sends it back in another authentication request.
    4. The Access Point decrypts the response. If this matches the challenge text, the Access Point sends back a positive reply.

## Slide 21: WEP Security Weakness
Open System: Transmitting the secret key uncrypted in the Management Frames
Shared Key: To decrypt data stream capturing the challenge frames in Sk-auth could derive the keystream and therefore the original key -> See WEP-Attacks later in the presentation
NEVER EVER USE WEP !!!

## Slide 22: Wi-Fi Protected Access WPA
WPA – IEEE 802.11i introduced in 2003
WPA-Personal aka WPA-PSK
  Primarily designed for Small/Home Office networks
  No authentication server required -> Use passphrase of 8 to 63 ASCII character
  Using ASCII charactes the 256-bit shared key is calculated by appliy PBKDF2 key derivation function to the passphrase, using SSID as the salt plus 4096 iterations of HMAC-SHA1
Notes: PBKDF2 applies a pseudorandom function, such as hash-based message authentication code (HMAC), to the input password or passphrase along with a salt value and repeats the process many times to produce a derived key, which can then be used as a cryptographic key in subsequent operations. The added computational work makes password cracking much more difficult, and is known as key stretching.
When the standard was written in the year 2000 the recommended minimum number of iterations was 1000, but the parameter is intended to be increased over time as CPU speeds increase. A Kerberos standard in 2005 recommended 4096 iterations;[3] Apple reportedly used 2000 for iOS 3, and 10000 for iOS 4;[4] while LastPass in 2011 used 5000 iterations for JavaScript clients and 100000 iterations for server-side hashing.[5]
Algorithmic representation of the iterative process of the Password Based Key Derivation Function 2.
Having a salt added to the password reduces the ability to use precomputed hashes (rainbow tables) for attacks, and means that multiple passwords have to be tested individually, not all at once. The standard recommends a salt length of at least 64 bits.[6] The US National Institute of Standards and Technology recommends a salt length of 128 bits.[7]

## Slide 23: WPA: Wi-Fi Protected Access
IEEE 802.11i – Overview
WPA 1
  Temporal Key Integrity Protocol – TKIP
  Message Integrity Check – Part of TKIP (Michael)
  Key Mixing – Part of TKIP
WPA 2
  Implementing Counter Mode Cipher Block Changing CCMP, an AES-based encryption mode
WPA 3
  Introduction of an Enterprise mode (AES-256 in GCM mode with SHA-384 as HMAC)
Notes: WPA2[edit]
Main article: IEEE 802.11i-2004
WPA2 replaced WPA. WPA2, which requires testing and certification by the Wi-Fi Alliance, implements the mandatory elements of IEEE 802.11i. In particular, it includes mandatory support for CCMP, an AES-based encryption mode.[7] [8] Certification began in September, 2004; from March 13, 2006, WPA2 certification is mandatory for all new devices to bear the Wi-Fi trademark.[9]
WPA3[edit]
See also: Opportunistic Wireless Encryption
In January 2018, the Wi-Fi Alliance announced WPA3 as a replacement to WPA2.[10][11]
The new standard uses an equivalent 192-bit cryptographic strength in WPA3-Enterprise mode[12] (AES-256 in GCM mode Galois Counter Mode with SHA-384 as HMAC), and still mandates the use of CCMP-128 (AES-128 in CCM mode) as the minimum encryption algorithm in WPA3-Personal mode.
The WPA3 standard also replaces the Pre-Shared Key exchange with Simultaneous Authentication of Equals as defined in IEEE 802.11-2016 resulting in a more secure initial key exchange in personal mode[13][14] and forward secrecy.[15] The Wi-Fi Alliance also claims that WPA3 will mitigate security issues posed by weak passwords and simplify the process of setting up devices with no display interface.[2][16]
Protection of management frames as specified in the IEEE 802.11w amendment is also enforced by the WPA3 specifications.

## Slide 24: WPA Terminology
WPA-Enterprise aka WPA-802.1X-2004 Mode
  Designed for enterprise networks using RADIUS
  Various Use of Extensible Authentication Protocol EAP, which is a authentication framework. There are almost 40 different methods available. Some of the most common are:
    EAP-Transport Layer Security -> EAE-TLS
    EAP Lightwight Extensible Authentication Protocol -> EAP-LEAP
    EAP Internet Key Excnage v.2 -> EAP-IKEv2
Wi-Fi Protected Setup WPS
  Mostly commercial products
  Easy key distribution methode but contains a major security hole via WPS PIN Recovery -> DO NOT USE IT !!
Notes: EAP Transport Layer Security (EAP-TLS), defined in RFC 5216, is an IETF open standard that uses the Transport Layer Security (TLS) protocol, and is well-supported among wireless vendors. EAP-TLS is the original, standard wireless LAN EAP authentication protocol.
EAP-TLS is still considered one of the most secure EAP standards available, although TLS provides strong security only as long as the user understands potential warnings about false credentials, and is universally supported by all manufacturers of wireless LAN hardware and software. Until April 2005, EAP-TLS was the only EAP type vendors needed to certify for a WPA or WPA2 logo.[5] There are client and server implementations of EAP-TLS in 3Com, Apple, Avaya, Brocade Communications, Cisco, Enterasys Networks, Fortinet, Foundry, Hirschmann, HP, Juniper, Microsoft, and open source operating systems. EAP-TLS is natively supported in Mac OS X 10.3 and above, wpa_supplicant, Windows 2000 SP4, Windows XP and above, Windows Mobile 2003 and above, Windows CE 4.2, and Apple's iOS mobile operating system.
Unlike most TLS implementations of HTTPS, such as on the World Wide Web, the majority of implementations of EAP-TLS require client-side X.509 certificates without giving the option to disable the requirement, even though the standard does not mandate their use.[6][7] Some have identified this as having the potential to dramatically reduce adoption of EAP-TLS and prevent "open" but encrypted access points.[6][7] On 22 August 2012 hostapd (and wpa_supplicant) added support in its Git repository for an UNAUTH-TLS vendor-specific EAP type (using the hostapd/wpa_supplicant project RFC 5612 Private Enterprise Number),[8] and on 25 February 2014 added support for the WFA-UNAUTH-TLS vendor-specific EAP type (using the Wi-Fi Alliance Private Enterprise Number),[9][10] which only do server authentication. This would allow for situations much like HTTPS, where a wireless hotspot allows free access and does not authenticate station clients but station clients wish to use encryption (IEEE 802.11i-2004 i.e. WPA2) and potentially authenticate the wireless hotspot. There have also been proposals to use IEEE 802.11u for access points to signal that they allow EAP-TLS using only server-side authentication, using the standard EAP-TLS IETF type instead of a vendor-specific EAP type.[11]
The requirement for a client-side certificate, however unpopular it may be, is what gives EAP-TLS its authentication strength and illustrates the classic convenience vs. security trade-off. With a client-side certificate, a compromised password is not enough to break into EAP-TLS enabled systems because the intruder still needs to have the client-side certificate; indeed, a password is not even needed, as it is only used to encrypt the client-side certificate for storage. The highest security available is when the "private keys" of client-side certificate are housed in smart cards.[12] This is because there is no way to steal a client-side certificate's corresponding private key from a smart card without stealing the card itself. It is more likely that the physical theft of a smart card would be noticed (and the smart card immediately revoked) than a (typical) password theft would be noticed. In addition, the private key on a smart card is typically encrypted using a PIN that only the owner of the smart card knows, minimizing its utility for a thief even before the card has been reported stolen and revoked.

## Slide 25: WPA: Wi-Fi Protected Access
EAP Method | Re-Keying | Mut.-Auth. | Clientcertificate | Tunnel | Standard | WPA comp
EAP-MD5 | NO | NO | NO | NO | YES | NO
LEAP | YES | YES | NO | NO | YES/NO | YES
EAP-TLS | YES | YES | YES | NO | YES | YES
PEAP | YES | YES | NO | YES | YES | YES
EAP-SIM | YES | YES | NO | NO | YES | YES
EAP-FAST | YES | YES | NO | YES | YES/NO | YES
Notes: EAP-FAST (Flexible Authentication via Secure Tunneling) was developed by Cisco*. Instead of using a certificate to achieve mutual authentication. EAP-FAST authenticates by means of a PAC (Protected Access Credential) which can be managed dynamically by the authentication server.

## Slide 26: Attack Vectors, Threats and Vulnerabilities
Traditional RF-Attacks
Radio Jamming
  Deliberate blocking or interference with authorized wireless communication
  Distinction between „jamming“ and „interference“
    Jamming describes the DELIBERATE Use of radio noise or signals in an attempt to disrupt communication
    Interference describes the UNINTENTIONAL forms of disruption due to malfunction or misconfiguration
In most countries jamming is highly illegal
=> DON´T DO IT !!

## Slide 27: Jamming

## Slide 28: Mobility Attack -> WARDRIVING
Wardriving is a form of reconnaissance
Usually used to find open Hotspots in towns, organisations, industrial plans, etc.
There are no laws that specifically prohibit or allow wardriving
Passive listening (Kismet or KisMAC) similar to listen /receiving radio signals from a TV/radio broadcast station
Another form is warbiking
https://vimeo.com/93257547

## Slide 29: Attack Vectors
In general, as Wi-Fi is just another OSI Layer 1 / Layer 2 technology attack vectors for TCP/IP and layer above still remains
  Denial of Service Attacks ( DoS or DDoS)
  Spoofing MAC Addresses
  Malware/Ransomware Attacks
  Advanced Persistance Threats – APTs
  Rootkits, RATs and Keylogger
  Social Engineering
Notes: RAT -> Remote Administration Tools … or better … Remote Access Trojaner (BackOrifice or Sub7)

## Slide 30: Attack Vectors
Wi-Fi specific Attacks > Trivial and non-trivial
Trivial:
  Access to an open Wi-Fi Network
  Access to Wi-Fi without actively sending SSID
  Access to Wi-Fi with MAC Filters
Non-Trivial:
  WPA 1/2/3 encrypted Wi-Fi Network
  Rogue Access Points
  Evil Twin Attacks
  KRACK
  IS WEP Cracking trivial? Lets have a look in detail…..
Notes: RAT -> Remote Administration Tools … or better … Remote Access Trojaner (BackOrifice or Sub7)

## Slide 31: WEP Attack 1/5
Getting the WEP Key via AP and STA
IV –> Initialization Vector -> concatinate with WEP-Key  Keystream
Problem: Avoid using the same IV while joining a Wi-Fi Network…. This can happens when hunderts of thousands repetition occour -> IV Collision
How to provoke a collision?
  Passive listening to hundreds of STA during long time
  ARP Replay Attack by using MAC Spoofing
Notes: Concatenate – Verkettung, Verknüpfung

## Slide 32: WEP Attack 2/5
Sniffed Paket 1 |  | 
Clear Text 1 |  | 1110 1011
Keystream 1 | XOR | 0101 1111
Secret Text 1 |  | 1011 0100
Sniffed Paket 2 |  | 
Clear Text 2 |  | 1100 0101
Keystream 2 | XOR | 0101 1111
Secret Text 2 |  | 1001 1010
Theoretical Example
XOR of Secret Texts |  | 
Secret Text 1 |  | 1011 0100
Secret Text 2 | XOR | 1001 1010
Result |  | 0010 1110
XOR of Clear Texts |  | 
Clear Text 1 |  | 1110 1011
Clear Text 2 | XOR | 1100 0101
Result |  | 0010 1110
Same Value
Notes: Concatenate – Verkettung, Verknüpfung

## Slide 33: WEP Attack 3/5
Proof to obtain Clear Text 2 |  | 
Result XOR Secret Texts |  | 0010 1110
Clear Text 1 | XOR | 1110 1011
Clear Text 2 |  | 1100 0101
Evidence and Proof
Assume, that Clear Text 1 and both Keystreams are known
IF
Clear Text + Keystream = Secret Text
THEN
Clear Text + Secret Text = Keystream
Known Plaintext Attack
Notes: Q: How to get the Cleartext

## Slide 34: WEP Attack 4/5
General technical concept of a WEP Attack
Usage of a WLAN hacking tool like Kismet-Newcore or Aircrack –NG
Target is to find a cleartext - two ways to accomplish
  Sending targeted packets to AP and forcing response
  Passive listening to standard procedures (e.g. Handshake TCP/IP or DHCP protocol)
Practical Example
Notes: Concatenate – Verkettung, Verknüpfung

## Slide 35: WEP Attack 5/5
Gathering/sniffing and storing Wi-Fi network traffic – minimum of 100.000 packets, better more depending of traffic volume and cracking computer power of attack PC ( Core i7/i9 – 3GHz+ – 16GRAM+ – GTX 1060/RX 480 above recommended)
  ARP Replay attack:
  aireplay –ng -3 –arpreplay –b <MACAddr AP> -h <MACAddr STA> -r Capfilename.cap wlan0
    -3 means standard arp request replay
Aircrack does the work – reading packets and counting the IVs
Searching for IVs and collisions
After a while aircrack provides the WEP key
Notes: Concatenate – Verkettung, Verknüpfung

## Slide 36: Attack Vectors
Non-Trivial:
  WPA 1/2/3 encrypted Wi-Fi Network
  Rogue Access Points
  Evil Twin Attacks
  KRACK
Notes: RAT -> Remote Administration Tools … or better … Remote Access Trojaner (BackOrifice or Sub7)

## Slide 37: Attack Vectors - WPA
WPA correctly implemented is very secure
Uses the AES encryption scheme…. Unbreakable so far ( unless post-quantum cryptoanalysis will work
Only way is to find weak PSKs (8-63 characters).
To start a WPA attack aka WPA Cracking makes sure that
  WLAN Router does not have standard password
  No WPS vulnarabilty exists
Dictionary Attack to find the PSK is most efficient
Notes: RAT -> Remote Administration Tools … or better … Remote Access Trojaner (BackOrifice or Sub7)

## Slide 38: Attack Vectors - Rogue APs
Nightmare of any Security/Network Administrator or IT-Security Manager
Hidden / Shadow IT Problem
Easy implementation by tethering (Smartphone, Tablets, Laptops,etc)
Connection via 4G to the Internet – Classic FWs or Webproxies fails
Protection: WiFi-IDS/IPS, SIEM and NG-Endpoint
ATTENTION: In PenTest Szenario get permission for using Rogue APs
In US and EU considered a severe act of espionage and cybercrime
Notes: RAT -> Remote Administration Tools … or better … Remote Access Trojaner (BackOrifice or Sub7)

## Slide 39: Attack Vectors - Evil Twin
Evil Twin Attack simply means there is another AP (Rogue) to pretend to be the correct and authorised AP to which a client can be connected
Often happens in Hotspots (Restaurants, Bars, Airports, etc.)
Providing Fake web-GUIs
A little bit of phishing required – social engineering
Good tool is wifiphiser (integrated in Kali Linux)
Notes: RAT -> Remote Administration Tools … or better … Remote Access Trojaner (BackOrifice or Sub7)

## Slide 40: Attack Vectors - KRACK
Key Reinstallation Attack -> KRACK
Replay Attack on WPA2 – CVE 2017-13077
Inherent vulnerabilty in the 4-way handshake of the Wi-Fi Protected Access II security protocol
Effects all major software platforms incl. Microsoft Windows, MacOS, iOS, Android, Linux, OpenBSD,etc.
How to protect?
  Install latest Patch from vendors -> might be very seldom
  Useage of WPA3: Replace PSK exhange with Simultaneous Authentification of Equals SAE
Notes: RAT -> Remote Administration Tools … or better … Remote Access Trojaner (BackOrifice or Sub7)

## Slide 41: Wi-Fi – How to protect? TOP 10 Rules for a secure WiFi-Network operation
Do not use Standard Passwords, SSIDs, Routerpasswords
Usage of strong passwords plus Passwordmanager
Only WPA2 or WPA3 for Authentification
Deactivate WPS
Enterprise environment -> WPA 2 Enterprise
Enterprise environment -> specialized Wi-Fi IDS and/or IPS
Multiple Wi-Fi Networks -> Guest-Wi-Fi, Conference-Room Wi-Fi, etc.
Usage of Protected Management Frames PMF
Home Wi-Fi: Changing PSK 1-4 times per year
Usage of Firewalls (Inbuild in SoHo Router or external/additional)
Notes: RAT -> Remote Administration Tools … or better … Remote Access Trojaner (BackOrifice or Sub7)

## Slide 42: FINISH
THANK YOU VERY MUCH FOR YOUR ATTENTION
YOURS
INGO ROSENBAUM
STAY HAPPY AND HEALTHY

## Slide 43: Sources
Books: WLAN Hacking: Tim Philip /Rico Walde – German Network Hacking: Dr. Peter Kraft/Andreas Weyert – German 802.11 Wirless Networks: Matthew S.Gast – English The Hacker Playbook 2: Peter Kim – English Wireshark 101: Laura Chappell All In One CISSP: Shon Harris
Links https://en.wikipedia.org/wiki/Wireless_security https://de.wikipedia.org/wiki/IEEE_802.11 https://en.wikipedia.org/wiki/Orthogonal_frequency-division_multiplexing https://en.wikipedia.org/wiki/Extensible_Authentication_Protocol<

## Slide 44: Sources
Video / Online Tutorials https://www.youtube.com/watch?v=qsmYD_6AeIU https://www.slideshare.net/AirTightWIPS/80211w-is-ratified-so-what-does-it-mean-for-your-wlan https://www.slideshare.net/wildpackets/80211-2012-update https://www.slideshare.net/oded1233/80211p?next_slideshow=1 https://www.youtube.com/watch?v=PHoLD91qE5A